A202 GRADE A,A202 Grade A Steel Plate,A202 GRADE A Supplier

Gangsteel Bolier Plate Factory are specialized in producing and exporting A202/A202M A202 Grade A NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A202 Grade A,A202/A202M A202 Grade A,A202 Grade A Steel Plate,A202 Grade A HIC,A202 Grade A Nace

Tags: A202 Grade A,A202/A202M A202 Grade A,A202 Grade A Steel Plate,A202 Grade A steel factory, A202 Grade A adopt standard, A202 Grade A Heat treatment, A202 Grade A Technical delivery condition, A202 Grade A Chemical, A202 Grade A Mechanical property, A202 Grade A Price, A202 Grade A CEV, A202 Grade A Impact degree, A202 Grade A impact energy, A202 Grade A Supplier,A202 Grade A Specification, A202 Grade A properties, Material A202 Grade A N, A202 Grade A Material, A202/A202M, A202 Grade A Steel, A202 Grade A Yield, A202 Grade A plate, A202 Grade A HIC, A202 Grade A NACE MR0175, A202 Grade A ISO 15156, A202 Grade A NACE MR0103, A202 Grade A SSC

Keyword: A202 GRADE A,A202 Grade A Steel Plate,A202 GRADE A Supplier

1.  A202 Grade A Adopt standard: ASMT A202/A202M Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon

2.  A202 Grade A Specification:  Thickness: 5mm to 200mm; Width: 1500mm to 3500mm: Length: 3000mm to 27000mm

3.  Third Party Inspection for A202 Grade A: ABS, DNV, BV, GL, CCS, LR, RINA, KR, NK, CE, SGS, IKE, IEI or other quality department.

4.  A202 Grade A Chemical composition % of the Product analysis of grade

| Grade | C % | P % | S% | Si% | Cr% | Mn% |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A202 Grade A | 0.17 | 0.035 | 0.035 | 0.54-0.96 | 0.31-0.64 | 0.97-1.52 |  |  |

5.  A202 Grade A Mechanical Property

| Grade | Min Yield | Tensile | Thicknesss | Elongation |
| --- | --- | --- | --- | --- |
| A202 Grade A | 310 Mpa | 515-655Mpa | <=50MM | 19% |
|  | 310 Mpa | 515-655Mpa | 50-200MM | 16% |

6.  Normally A202/A202M A202 Grade A plates are normally supplied in the as-rolled condition. The plates may be ordered normalized or stress relieved, or both.

7.  A202 Grade A Delivery Time Or Lead Time: 20-35days

8.  A202 Grade A Extra Service: Pretreatment (Shot Blasting, Sand Blast, Painting and Galvanized), Cutting Parts, Sample Service, Third Party inspection, UT Test and Size inspection.

9.  If you have any requirement in steel plate for A202 Grade A, whether the new plate or stock list of material, please feel free to contact us by email of calling.

If you had any question at our plate or service. Please contact our after service department to get faster reply

.

Gangsteel Group Company Principle

More Cheaper Price,

More Faster Delivery,

The Best Company Prestige,

The Best After sales service,

The One step Steel material Solution

The Best Professional quality control system

Supplementary Requirements

S2. Product Analysis,       S8: Ultrasonic Examination

S3: Simulated pos-weld heat treatment of mechanical

S15: Reduction of area measurement and test coupons

S18: Maximum Tensile strength

S6: Drop weight test

S30：Charpy V notch impact test for structural shapes

Welcome to Gangsteel Group and any requirement in steel material, please feel free to contact us.

Gangsteel Bolier Plate Factory are specialized in producing and exporting A202/A202M A202 Grade A NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A202 Grade A,A202/A202M A202 Grade A,A202 Grade A Steel Plate,A202 Grade A HIC,A202 Grade A Nace

Tags: A202 Grade A,A202/A202M A202 Grade A,A202 Grade A Steel Plate,A202 Grade A steel factory, A202 Grade A adopt standard, A202 Grade A Heat treatment, A202 Grade A Technical delivery condition, A202 Grade A Chemical, A202 Grade A Mechanical property, A202 Grade A Price, A202 Grade A CEV, A202 Grade A Impact degree, A202 Grade A impact energy, A202 Grade A Supplier,A202 Grade A Specification, A202 Grade A properties, Material A202 Grade A N, A202 Grade A Material, A202/A202M, A202 Grade A Steel, A202 Grade A Yield, A202 Grade A plate, A202 Grade A HIC, A202 Grade A NACE MR0175, A202 Grade A ISO 15156, A202 Grade A NACE MR0103, A202 Grade A SSC