A283GRB,A283GRB Steel Plate,A283GRB Supplier

Gangsteel Bolier Plate Factory are specialized in producing and exporting A283/A283M A283GRB NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A283GRB,A283/A283M A283GRB,A283GRB Steel Plate,A283GRB HIC,A283GRB Nace

Tags: A283GRB,A283/A283M A283GRB,A283GRB Steel Plate,A283GRB steel factory, A283GRB adopt standard, A283GRB Heat treatment, A283GRB Technical delivery condition, A283GRB Chemical, A283GRB Mechanical property, A283GRB Price, A283GRB CEV, A283GRB Impact degree, A283GRB impact energy, A283GRB Supplier,A283GRB Specification, A283GRB properties, Material A283GRB N, A283GRB Material, A283/A283M, A283GRB Steel, A283GRB Yield, A283GRB plate, A283GRB HIC, A283GRB NACE MR0175, A283GRB ISO 15156, A283GRB NACE MR0103, A283GRB SSC

Keyword: A283GRB,A283GRB Steel Plate,A283GRB Supplier

1.  A283GRB Adopt standard: ASMT A283/A283M Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon

2.  A283GRB Specification:  Thickness: 5mm to 200mm; Width: 1500mm to 3500mm: Length: 3000mm to 27000mm

3.  Third Party Inspection for A283GRB: ABS, DNV, BV, GL, CCS, LR, RINA, KR, NK, CE, SGS, IKE, IEI or other quality department.

4.  A283GRB Chemical composition % of the Product analysis of grade

| Grade | C % | Mn % | P% | S% | Cu%(min) | Cu%(<=40mm) | Cu%(>40mm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A283GRB | 0.17 | 0.9 | 0.035 | 0.04 | 0.2 | 0.4 | 0.15-0.4 |

5.  A283GRB Mechanical Property

| Grade | Min Yield | Tensile | Thicknesss | Elongation |
| --- | --- | --- | --- | --- |
| A283GRB | 185 Mpa | 345-450Mpa | <=50MM | 28% |
|  | 185Mpa | 345-450Mpa | 50-200MM | 25% |

6.  Normally A283/A283M A283GRB plates are normally supplied in the as-rolled condition. The plates may be ordered normalized or stress relieved, or both.

7.  A283GRB Delivery Time Or Lead Time: 20-35days

8.  A283GRB Extra Service: Pretreatment (Shot Blasting, Sand Blast, Painting and Galvanized), Cutting Parts, Sample Service, Third Party inspection, UT Test and Size inspection.

9.  If you have any requirement in steel plate for A283GRB, whether the new plate or stock list of material, please feel free to contact us by email of calling.

If you had any question at our plate or service. Please contact our after service department to get faster reply

.

Gangsteel Group Company Principle

More Cheaper Price,

More Faster Delivery,

The Best Company Prestige,

The Best After sales service,

The One step Steel material Solution

The Best Professional quality control system

Supplementary Requirements

S2. Product Analysis,       S8: Ultrasonic Examination

S3: Simulated pos-weld heat treatment of mechanical

S15: Reduction of area measurement and test coupons

S18: Maximum Tensile strength

S6: Drop weight test

S30：Charpy V notch impact test for structural shapes

Welcome to Gangsteel Group and any requirement in steel material, please feel free to contact us.

Gangsteel Bolier Plate Factory are specialized in producing and exporting A283/A283M A283GRB NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A283GRB,A283/A283M A283GRB,A283GRB Steel Plate,A283GRB HIC,A283GRB Nace

Tags: A283GRB,A283/A283M A283GRB,A283GRB Steel Plate,A283GRB steel factory, A283GRB adopt standard, A283GRB Heat treatment, A283GRB Technical delivery condition, A283GRB Chemical, A283GRB Mechanical property, A283GRB Price, A283GRB CEV, A283GRB Impact degree, A283GRB impact energy, A283GRB Supplier,A283GRB Specification, A283GRB properties, Material A283GRB N, A283GRB Material, A283/A283M, A283GRB Steel, A283GRB Yield, A283GRB plate, A283GRB HIC, A283GRB NACE MR0175, A283GRB ISO 15156, A283GRB NACE MR0103, A283GRB SSC