A283GRC,A283GRC Steel Plate,A283GRC Supplier

Gangsteel Bolier Plate Factory are specialized in producing and exporting A283/A283M A283GRC NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A283GRC,A283/A283M A283GRC,A283GRC Steel Plate,A283GRC HIC,A283GRC Nace

Tags: A283GRC,A283/A283M A283GRC,A283GRC Steel Plate,A283GRC steel factory, A283GRC adopt standard, A283GRC Heat treatment, A283GRC Technical delivery condition, A283GRC Chemical, A283GRC Mechanical property, A283GRC Price, A283GRC CEV, A283GRC Impact degree, A283GRC impact energy, A283GRC Supplier,A283GRC Specification, A283GRC properties, Material A283GRC N, A283GRC Material, A283/A283M, A283GRC Steel, A283GRC Yield, A283GRC plate, A283GRC HIC, A283GRC NACE MR0175, A283GRC ISO 15156, A283GRC NACE MR0103, A283GRC SSC

Keyword: A283GRC,A283GRC Steel Plate,A283GRC Supplier

1.  A283GRC Adopt standard: ASMT A283/A283M Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon

2.  A283GRC Specification:  Thickness: 5mm to 200mm; Width: 1500mm to 3500mm: Length: 3000mm to 27000mm

3.  Third Party Inspection for A283GRC: ABS, DNV, BV, GL, CCS, LR, RINA, KR, NK, CE, SGS, IKE, IEI or other quality department.

4.  A283GRC Chemical composition % of the Product analysis of grade

| Grade | C % | Mn % | P% | S% | Cu%(min) | Cu%(<=40mm) | Cu%(>40mm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A283GRC | 0.24 | 0.9 | 0.035 | 0.04 | 0.2 | 0.4 | 0.15-0.4 |

5.  A283GRC Mechanical Property

| Grade | Min Yield | Tensile | Thicknesss | Elongation |
| --- | --- | --- | --- | --- |
| A283GRC | 205 Mpa | 380-515Mpa | <=50MM | 25% |
|  | 205Mpa | 380-515Mpa | 50-200MM | 22% |

6.  Normally A283/A283M A283GRC plates are normally supplied in the as-rolled condition. The plates may be ordered normalized or stress relieved, or both.

7.  A283GRC Delivery Time Or Lead Time: 20-35days

8.  A283GRC Extra Service: Pretreatment (Shot Blasting, Sand Blast, Painting and Galvanized), Cutting Parts, Sample Service, Third Party inspection, UT Test and Size inspection.

9.  If you have any requirement in steel plate for A283GRC, whether the new plate or stock list of material, please feel free to contact us by email of calling.

If you had any question at our plate or service. Please contact our after service department to get faster reply

.

Gangsteel Group Company Principle

More Cheaper Price,

More Faster Delivery,

The Best Company Prestige,

The Best After sales service,

The One step Steel material Solution

The Best Professional quality control system

Supplementary Requirements

S2. Product Analysis,       S8: Ultrasonic Examination

S3: Simulated pos-weld heat treatment of mechanical

S15: Reduction of area measurement and test coupons

S18: Maximum Tensile strength

S6: Drop weight test

S30：Charpy V notch impact test for structural shapes

Welcome to Gangsteel Group and any requirement in steel material, please feel free to contact us.

Gangsteel Bolier Plate Factory are specialized in producing and exporting A283/A283M A283GRC NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A283GRC,A283/A283M A283GRC,A283GRC Steel Plate,A283GRC HIC,A283GRC Nace

Tags: A283GRC,A283/A283M A283GRC,A283GRC Steel Plate,A283GRC steel factory, A283GRC adopt standard, A283GRC Heat treatment, A283GRC Technical delivery condition, A283GRC Chemical, A283GRC Mechanical property, A283GRC Price, A283GRC CEV, A283GRC Impact degree, A283GRC impact energy, A283GRC Supplier,A283GRC Specification, A283GRC properties, Material A283GRC N, A283GRC Material, A283/A283M, A283GRC Steel, A283GRC Yield, A283GRC plate, A283GRC HIC, A283GRC NACE MR0175, A283GRC ISO 15156, A283GRC NACE MR0103, A283GRC SSC