A841CL3,A841CL3 Steel Plate,A841CL3 Supplier

Gangsteel Bolier Plate Factory are specialized in producing and exporting SA-841/SA-841M A841CL3 NACE MR0175, MR0103 Boiler steel plate, Specification for Steel plates for pressure vessels,produced by the thermo mechanical control process(TMCP) Which is a large steel plate supplier mill at Gangsteel Group. A841CL3,SA-841/SA-841M A841CL3,A841CL3 Steel Plate,A841CL3 HIC,A841CL3 Nace

Tags: A841CL3,SA-841/SA-841M A841CL3,A841CL3 Steel Plate,A841CL3 steel factory, A841CL3 adopt standard, A841CL3 Heat treatment, A841CL3 Technical delivery condition, A841CL3 Chemical, A841CL3 Mechanical property, A841CL3 Price, A841CL3 CEV, A841CL3 Impact degree, A841CL3 impact energy, A841CL3 Supplier,A841CL3 Specification, A841CL3 properties, Material A841CL3 N, A841CL3 Material, SA-841/SA-841M, A841CL3 Steel, A841CL3 Yield, A841CL3 plate, A841CL3 HIC, A841CL3 NACE MR0175, A841CL3 ISO 15156, A841CL3 NACE MR0103, A841CL3 SSC

Keyword: A841CL3,A841CL3 Steel Plate,A841CL3 Supplier

1.  A841CL3 Adopt standard: ASMT SA-841/SA-841M Specification for Steel plates for pressure vessels,produced by the thermo mechanical control process(TMCP)

2.  A841CL3 Specification:  Thickness: 5mm to 200mm; Width: 1500mm to 3500mm: Length: 3000mm to 27000mm

3.  Third Party Inspection for A841CL3: ABS, DNV, BV, GL, CCS, LR, RINA, KR, NK, CE, SGS, IKE, IEI or other quality department.

4.  A841CL3 Chemical composition % of the Product analysis of grade

| Grade | C % | Mn %(<40mm) | P% | S% | Si% | Cu% | Ni% | Cr |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A841CL3 | 0.09 | 1.0-2.0 | 0.01 | 0.005 | 0.05-0.25 | 0.5 | 1.0-5.0 | 0.3 |
|  | Mo% | Cb% | V% | Mn %(>40mm) | Ti% | B% |  |  |
|  | 0.4 | 0.05 | 0.02 | -- | 0.006-0.03 | 0.0005-0.002 |  |  |

5.  A841CL3 Mechanical Property

| Grade | Min Yield | Tensile | Thicknesss | Elongation |
| --- | --- | --- | --- | --- |
| A841CL3 | 690 Mpa | 1000-1170Mpa | <40MM | 13% |
|  | -- | -- | 40-65MM | -- |
|  | -- | -- | >65MM | -- |

6.  Normally SA-841/SA-841M A841CL3 plates are normally supplied in the as-rolled condition. The plates may be ordered normalized or stress relieved, or both.

7.  A841CL3 Delivery Time Or Lead Time: 20-35days

8.  A841CL3 Extra Service: Pretreatment (Shot Blasting, Sand Blast, Painting and Galvanized), Cutting Parts, Sample Service, Third Party inspection, UT Test and Size inspection.

9.  If you have any requirement in steel plate for A841CL3, whether the new plate or stock list of material, please feel free to contact us by email of calling.

If you had any question at our plate or service. Please contact our after service department to get faster reply

.

Gangsteel Group Company Principle

More Cheaper Price,

More Faster Delivery,

The Best Company Prestige,

The Best After sales service,

The One step Steel material Solution

The Best Professional quality control system

Supplementary Requirements

S2. Product Analysis,       S8: Ultrasonic Examination

S3: Simulated pos-weld heat treatment of mechanical

S15: Reduction of area measurement and test coupons

S18: Maximum Tensile strength

S6: Drop weight test

S30：Charpy V notch impact test for structural shapes

Welcome to Gangsteel Group and any requirement in steel material, please feel free to contact us.

Gangsteel Bolier Plate Factory are specialized in producing and exporting SA-841/SA-841M A841CL3 NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A841CL3,SA-841/SA-841M A841CL3,A841CL3 Steel Plate,A841CL3 HIC,A841CL3 Nace

Tags: A841CL3,SA-841/SA-841M A841CL3,A841CL3 Steel Plate,A841CL3 steel factory, A841CL3 adopt standard, A841CL3 Heat treatment, A841CL3 Technical delivery condition, A841CL3 Chemical, A841CL3 Mechanical property, A841CL3 Price, A841CL3 CEV, A841CL3 Impact degree, A841CL3 impact energy, A841CL3 Supplier,A841CL3 Specification, A841CL3 properties, Material A841CL3 N, A841CL3 Material, SA-841/SA-841M, A841CL3 Steel, A841CL3 Yield, A841CL3 plate, A841CL3 HIC, A841CL3 NACE MR0175, A841CL3 ISO 15156, A841CL3 NACE MR0103, A841CL3 SSC