A202GRB,A202GRB Steel Plate,A202GRB Supplier

Gangsteel Bolier Plate Factory are specialized in producing and exporting A202/A202M A202GRB NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A202GRB,A202/A202M A202GRB,A202GRB Steel Plate,A202GRB HIC,A202GRB Nace

Tags: A202GRB,A202/A202M A202GRB,A202GRB Steel Plate,A202GRB steel factory, A202GRB adopt standard, A202GRB Heat treatment, A202GRB Technical delivery condition, A202GRB Chemical, A202GRB Mechanical property, A202GRB Price, A202GRB CEV, A202GRB Impact degree, A202GRB impact energy, A202GRB Supplier,A202GRB Specification, A202GRB properties, Material A202GRB N, A202GRB Material, A202/A202M, A202GRB Steel, A202GRB Yield, A202GRB plate, A202GRB HIC, A202GRB NACE MR0175, A202GRB ISO 15156, A202GRB NACE MR0103, A202GRB SSC

Keyword: A202GRB,A202GRB Steel Plate,A202GRB Supplier

1.  A202GRB Adopt standard: ASMT A202/A202M Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon

2.  A202GRB Specification:  Thickness: 5mm to 200mm; Width: 1500mm to 3500mm: Length: 3000mm to 27000mm

3.  Third Party Inspection for A202GRB: ABS, DNV, BV, GL, CCS, LR, RINA, KR, NK, CE, SGS, IKE, IEI or other quality department.

4.  A202GRB Chemical composition % of the Product analysis of grade

| Grade | C % | Mn % | P% | Si% | Cr% |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A202GRB | 0.25 | 0.97-1.52 | 0.035 | 0.54-0.96 | 0.31-0.64 |  |  |  |

5.  A202GRB Mechanical Property

| Grade | Min Yield | Tensile | Thicknesss | Elongation |
| --- | --- | --- | --- | --- |
| A202GRB | 325 Mpa | 585-760Mpa | <=50MM | 18% |
|  | 325 Mpa | 585-760Mpa | 50-200MM | 15% |

6.  Normally A202/A202M A202GRB plates are normally supplied in the as-rolled condition. The plates may be ordered normalized or stress relieved, or both.

7.  A202GRB Delivery Time Or Lead Time: 20-35days

8.  A202GRB Extra Service: Pretreatment (Shot Blasting, Sand Blast, Painting and Galvanized), Cutting Parts, Sample Service, Third Party inspection, UT Test and Size inspection.

9.  If you have any requirement in steel plate for A202GRB, whether the new plate or stock list of material, please feel free to contact us by email of calling.

If you had any question at our plate or service. Please contact our after service department to get faster reply

.

Gangsteel Group Company Principle

More Cheaper Price,

More Faster Delivery,

The Best Company Prestige,

The Best After sales service,

The One step Steel material Solution

The Best Professional quality control system

Supplementary Requirements

S2. Product Analysis,       S8: Ultrasonic Examination

S3: Simulated pos-weld heat treatment of mechanical

S15: Reduction of area measurement and test coupons

S18: Maximum Tensile strength

S6: Drop weight test

S30：Charpy V notch impact test for structural shapes

Welcome to Gangsteel Group and any requirement in steel material, please feel free to contact us.

Gangsteel Bolier Plate Factory are specialized in producing and exporting A202/A202M A202GRB NACE MR0175, MR0103 Boiler steel plate, Standard Specification for Pressure Vessel Plates, Alloy Steel, Chromium-Manganese-Silicon Which is a large steel plate supplier mill at Gangsteel Group. A202GRB,A202/A202M A202GRB,A202GRB Steel Plate,A202GRB HIC,A202GRB Nace

Tags: A202GRB,A202/A202M A202GRB,A202GRB Steel Plate,A202GRB steel factory, A202GRB adopt standard, A202GRB Heat treatment, A202GRB Technical delivery condition, A202GRB Chemical, A202GRB Mechanical property, A202GRB Price, A202GRB CEV, A202GRB Impact degree, A202GRB impact energy, A202GRB Supplier,A202GRB Specification, A202GRB properties, Material A202GRB N, A202GRB Material, A202/A202M, A202GRB Steel, A202GRB Yield, A202GRB plate, A202GRB HIC, A202GRB NACE MR0175, A202GRB ISO 15156, A202GRB NACE MR0103, A202GRB SSC